## Slide 1
Dynamic Host Configuration Protocol
DHCP
Muna Sikder
Computer Science and Engineering,
University of Dhaka.
Teleinformática y Comunicaciones

## Slide 2: DHCP
‘Dynamic Host Configuration Protocol’ is a means for networked devices to get their TCP/IP networking settings from a central server.
DHCP assigns IP addresses and other configuration parameters automatically.

## Slide 3: Dynamic Assignment of IP addresses
Dynamic assignment of IP addresses is desirable for several reasons:
  IP addresses are assigned on-demand
  Avoid manual IP configuration
  Support mobility of laptops
Three Protocols:
  RARP (until 1985, no longer used)
  BOOTP (1985-1993)
  DHCP (since 1993)
Only DHCP is widely used today.

## Slide 4: Motivation for DHCP
Configuration parameters for network hosts
      IP address
      Router’s IP address
      Subnet Mask
      IP address of a DNS server
  Those information is dependent on the individual configuration of the network.
  What about a diskless workstation or a computer with a disk that is booted for the first time?

## Slide 5: Motivation for DHCP(cont..)
Before DHCP
          RARP
          BOOTP
Problems of RARP
  Provides only the IP address
  RARP client and server must be on the same network because of it is a data link layer service.
Problems of BOOTP
  Is a static configuration protocol

## Slide 6: DHCP provides
DHCP supports three models:
    Dynamic allocation
    Automatic or Reserved allocation
    Static allocation
DHCP is backward compatible with BOOTP.
Is a application layer protocol.
Port for both protocol:
        client : UDP, 68
        Server : UDP,67
Notes: Dynamic allocation: Server chooses and allocates an IP address with finite lease.
Automatic or Reserved allocation: Server allocates an IP address with infinite lease.
Static allocation: Server allocates an IP address that has been chosen by the administrator.

## Slide 7: Simple network
Hello Mr. Server, I need to connect to the Internet, could you be kind to hook me up with an IP address?
Ok dude, I got some in my pool of address, I lend you it. Check it out?
Your IP : 123.45.78.6
Thank you Mr. Server, I like your offer. I will use it.
You’re welcome, here is your configuration but it’s only for 3 days.
DHCP server discover
DHCP server offer
DHCP request
DHCP acknowledge
Router
Internet
DHCP Server
UDP Port 68
UDP Port 68
UDP Port 68
UDP Port 67
DHCP Clients
DHCP protocol is a mainly 4-step process:
DHCP Server
DHCP Clients
Broadcast
Unicast

## Slide 8: DHCP Message Types
DHCP Message | Use
DHCPDISCOVER | Client broadcast to locate available servers
DHCPOFFER | Server to client response offering configuration parameters
DHCPREQUEST | Client broadcast requesting offered parameters
DHCPDECLINE | Client to server notification that IP address is in use
DHCPACK | Server to client response confirming a request
DHCPNAK | Server to client response denying a request
DHCPRELEASE | Client to server request to relinquish IP address
DHCPINFORM | Client to server request for configuration parameters

## Slide 9: DHCP transition diagram
Initializing
Rebinding
Renewing
Requesting
Bound
Selecting
Boot
DHCPDISCOVER
DHCPREQUEST
DHCPACK
DHCPOFFER
DHCPACK
DHCPACK
DHCPRELEASE
DHCPREQUEST
Lease time 50% expired
Lease time 87.5% expired
DHCPREQUEST
Lease time expired
DHCPNACK

## Slide 10: DHCP transition diagram..
Initializing
Boot

## Slide 11: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
Source IP : 0.0.0.0
Source MAC : EA.0D.45.B4
Destination IP : 1.1.1.1
68
UDP
open

## Slide 12: DHCP transition diagram..
Initializing
Boot
Selecting
DHCPDISCOVER

## Slide 13: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
Source IP : 0.0.0.0
Source MAC : EA.0D.45.B4
Destination IP : 1.1.1.1
DHCPOFFER
Source IP : 122.45.78.3
Destination IP : 1.1.1.1
Des MAC : EA.0D.45.B4
Client IP : 122.45.67.23
68
UDP

## Slide 14: DHCP transition diagram..
Initializing
Boot
DHCPDISCOVER
Selecting
DHCPOFFER

## Slide 15: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
Source IP : 0.0.0.0
Source MAC : EA.0D.45.B4
Destination IP : 1.1.1.1
DHCPOFFER
Source IP : 122.45.78.3
Destination IP : 1.1.1.1
Des MAC : EA.0D.45.B4
Client IP : 122.45.67.23
DHCPREQUEST
Accept ,request to bind client physical address and its offered IP
68
UDP

## Slide 16: DHCP transition diagram..
Initializing
Boot
DHCPDISCOVER
Requesting
DHCPREQUEST
Selecting
DHCPOFFER

## Slide 17
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCACK
After receiving the ACK, client use offered IP.
68
UDP

## Slide 18
Requesting
Initializing
Boot
DHCPDISCOVER
DHCPREQUEST
Bound
DHCPACK
Selecting
DHCPOFFER
DHCP transition diagram..

## Slide 19
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCACK
After receiving the ACK, client use offered IP.
DHCPREQUEST
After 50% of lease time expires
DHCPREQUEST
If the server does not respond, the request is repeated.
If server responds with a NACK client must start all over again.i
68
UDP

## Slide 20: DHCP transition diagram..
Requesting
Initializing
Boot
DHCPDISCOVER
DHCPREQUEST
Bound
DHCPACK
Selecting
DHCPOFFER
Renewing
DHCPREQUEST
Lease time 50% expired
DHCPRELEASE

## Slide 21: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCPACK
DHCREQUEST
DHCPACK
68
UDP

## Slide 22: DHCP transition diagram..
Initializing
Requesting
Bound
Selecting
Boot
DHCPDISCOVER
DHCPREQUEST
DHCPACK
DHCPOFFER
DHCPACK
Renewing
DHCPREQUEST
Lease time 50% expired
DHCPRELEASE
Lease cancelled/

## Slide 23: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCPACK
DHCREQUEST
DHCPACK
DHCPREQUEST
Before 87.5% of lease time expires
68
UDP

## Slide 24: DHCP transition diagram..
Initializing
Requesting
Bound
Selecting
Boot
DHCPDISCOVER
DHCPREQUEST
DHCPACK
DHCPOFFER
DHCPACK
Renewing
DHCPREQUEST
Lease time 50% expired
Rebinding
Lease time 87.5% expired
DHCPREQUEST
DHCPRELEASE

## Slide 25: DHCP transition..
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCPACK
DHCREQUEST
DHCPACK
DHCPREQUEST
Before 87.5% of lease time expires
DHCACK/ DHCPNACK
68
UDP

## Slide 26: DHCP transition diagram..
Initializing
Rebinding
Requesting
Selecting
Boot
DHCPDISCOVER
DHCPREQUEST
DHCPACK
DHCPOFFER
DHCPACK
DHCPACK
Renewing
DHCPREQUEST
Lease time 50% expired
Lease time 87.5% expired
DHCPREQUEST
Bound
Lease time expired/
DHCPNACK
DHCPRELEASE

## Slide 27: DHCP transition
DHCP Client
DHCP Server
67
UDP
122.45.78.3
DHCPDISCOVER
DHCPOFEER
DHCREQUEST
DHCPACK
DHCREQUEST
DHCPACK
DHCACK/ DHCPNACK
DHCREQUEST
DHCPRELEASE
68
UDP
After 50% time expires
After 87.50% time expires

## Slide 28: DHCP transition diagram
Initializing
Rebinding
Requesting
Selecting
Boot
DHCPDISCOVER
DHCPREQUEST
DHCPACK
DHCPOFFER
DHCPACK
DHCPACK
Renewing
DHCPREQUEST
Lease time 50% expired
Lease time 87.5% expired
DHCPREQUEST
Bound
Lease time expired/
DHCPNACK
DHCPRELEASE

## Slide 29: Example with Relay Agent
Router
Internet
Relay agent
Router
67
UDP
Broadcast
Source123.45.67.8
Destination : 1.1.1.1
Client IP : 123.45.68.7
DHCPOFFER
123.45.67.8
Broadcast
Source : 0.0.0.0
Destination : 1.1.1.1
DHCPDISCOVER
Unicast
Source : 123.45.67.8
Destination : 123.45.55.3
Unicast
Source : 123.45.67.8
Destination : 123.45.55.3
DHCP Server
123.45.55.3
Unicast
Source : 123.45.67.8
Destination : 123.45.55.3
Client IP: 123.45.68.7
DHCPOFFER
Unicast
Source : 123.45.53
Destination : 123.45.68
Client IP : 123.45.68.7
New DHCP Client
68
UDP

## Slide 30: Another Example
UDP Port 68
UDP Port 68
UDP Port 68
DHCP Clients
Broadcast DHCPDISCOVER
Broadcast DHCPDISCOVER
Source : 0.0.0.0
Destination : 1.1.1.1
Source : 0.0.0.0
Destination : 1.1.1.1
Both packets are same. How does server distinguish which packet come from which client?
Broadcast DHCPOFFER
Source : 123.45.68.7
Destination : 1.1.1.1
Client IP : 123.45.55.8
DHCP Server
UDP Port 67
123.45.68.7
For this problem server can offer same IP for both.
Broadcast DHCPOFFER
Source : 123.45.68.7
Destination : 1.1.1.1
Client IP : 123.45.55.8
To overcome this problem, client uses Transaction ID.
Broadcast DHCPDISCOVER
Broadcast DHCPDISCOVER
Source : 0.0.0.0
Destination : 1.1.1.1
Transaction ID : E1CA52AD
Source : 0.0.0.0
Destination : 1.1.1.1
Transaction ID : A3C5A2CB
Broadcast DHCPOFFER
Source : 123.45.68.7
Destination : 1.1.1.1
Client IP : 123.45.55.23
Transaction ID : E1CA52AD
Broadcast DHCPOFFER
Source : 123.45.68.7
Destination : 1.1.1.1
Client IP : 123.45.55.8
Transaction ID : A3C5A2CB
Notes: Randomly choose transaction ID.

## Slide 31: Another situation
Internet
DHCP Server
UDP Port 67
DHCP Clients
DHCP Server
123.45.55.3
Relay agent
123.45.67.8
67
UDP
DHCPDISCOVER
DHCPDISCOVER
DHCPDISCOVER
DHCPDISCOVER
UDP Port 67
120.45.55.3
DHCPOFFER
DHCPOFFER
DHCPOFFER
DHCPOFFER
Client receives this offer and sends DHCPREQUEST packet.
DHCPOFFER
DHCREQUEST
Discard
New DHCP client
DHCPOFFER
DHCPOFFER
?
Router

## Slide 32: DHCP message format (cont.)
Operation Code | Hardware Type | Hardware Length |  | Hop Count
Transaction ID |  |  |  | 
Seconds Elapsed |  | F | Must Be Zero (MBZ) | 
Client IP address |  |  |  | 
Your IP address |  |  |  | 
Server IP address |  |  |  | 
Gateway IP address |  |  |  | 
Client hardware address (16 bytes) |  |  |  | 
Server host name (64 bytes) |  |  |  | 
Boot file name (128 bytes) |  |  |  | 
Options (up to 312 bytes) |  |  |  | 
32 Bits

## Slide 33: DHCP message format
Option code – defines the type of packet : request(1) or reply(2)
Transaction ID - a random number that is used by the client to match incoming DHCP messages with pending requests.
Gateway IP address – contains the IP address of the router filled by the server in reply message.
Client IP address - used when client knows its IP address.
Your IP address - the DHCP server will place the offered client IP address in this field, if the client IP address is 0.0.0.0.
Server IP address - the DHCP server address, if it is known. Otherwise, it is used in DHCPOFFER and DHCPACK.
Boot filename – contains a string consisting of the full pathname of the boot file. Client can use this path to retrieve other booting information.
Options – it can carry either additional information or some specific vendor information.

## Slide 34: Conclusion
DHCP is a dynamic configure protocol with two database : one is similar to BOOTP and other is a pool of IP address available for temporary assignment. DHCP server issues a lease for an IP address to a client for a specific period of time. DHCP packet format is similar to that of BOOTP. DHCP should not require a server on each sub-net. Relay agent that is compatible with BOOTP can be used.
NIP (Network Information Protocol) has the mechanism of dynamic allocation. When the NIP client requests an IP address, NIP server returns a set of IP address that is available in the network. NIP client selects one IP address from the network, and checks its availability with ARP.

## Slide 35
FIN
Router
Internet
DHCP Server
UDP Port 68
UDP Port 68
UDP Port 68
UDP Port 67
DHCP Clients